## Slide 1: Praktikum 1 Visi Komputer dan Pengolahan Citra
Firnanda Pristiana Nurmaida (112200008 / S2 TE)

## Slide 2: Program 1 Kamera Minoru
import numpy as np
import cv2
left_camera = cv2.VideoCapture(4)
right_camera = cv2.VideoCapture(6)
# id cam l = 4
# id cam r = 6
# Check if the cameras opened successfully
if not left_camera.isOpened() or not right_camera.isOpened():
print("Error: Unable to open one or both cameras")
exit()
stereo = cv2.StereoSGBM_create(numDisparities=3, blockSize=15)
Membuka kamera sebelah kanan dan kiri
Apakah kamera telah berhasil terbuka?
Membuat objek stereo SGBM

## Slide 3
while True:
ret1, left_frame = left_camera.read()
ret2, right_frame = right_camera.read()
if not (ret1 and ret2):
break
left_gray = cv2.cvtColor(left_frame, cv2.COLOR_BGR2GRAY)
right_gray = cv2.cvtColor(right_frame, cv2.COLOR_BGR2GRAY)
try:
disparity = stereo.compute(left_gray, right_gray) + 0.0000001
except cv2.error as e:
print(f"Error computing disparity: {e}")
continue
Mengambil frame dari kedua kamera
Konversi ke abu-abu
Menghitung disparit

## Slide 4
depth = 1.0 / disparity
cv2.imshow('Camera Laptop', left_frame)
cv2.imshow('Camera HP', right_frame)
cv2.imshow('Depth Map', depth)
if cv2.waitKey(1) & 0xFF == ord('q'):
break
left_camera.release()
right_camera.release()
cv2.destroyAllWindows()
Menghitung jarak ke objek, Faktor konversi yang bergantung pada konfigurasi kamera
Menampilkan citra kedua kamera dan citra kedalaman

## Slide 5: Program Minoru Dilengkapi Disparity Map
import cv2
import numpy as np
# Open the left and right cameras (modify indices if needed)
left_cap = cv2.VideoCapture(4)
right_cap = cv2.VideoCapture(6)
# Check if the cameras opened successfully
if not left_cap.isOpened() or not right_cap.isOpened():
print("Error: Could not open one or both cameras.")
exit()
# Set up stereo block matching parameters (adjust as needed)
stereo = cv2.StereoBM_create(numDisparities=16, blockSize=5)
Membuka kamera sebelah kanan dan kiri
Apakah kamera berhasil dibuka?
Mengatur parameter stereo block matching

## Slide 6
while True:
# Read frames from both cameras
ret1, left_frame = left_cap.read()
ret2, right_frame = right_cap.read()
# Check if both frames were read successfully
if not ret1 or not ret2:
print("Error: Could not read frames from one or both cameras.")
break
# Convert frames to grayscale
left_gray = cv2.cvtColor(left_frame, cv2.COLOR_BGR2GRAY)
right_gray = cv2.cvtColor(right_frame, cv2.COLOR_BGR2GRAY)
Membaca kamera kanan dan kiri
Apakah kamera berhasil terbaca?
Konversi frame ke grayscale

## Slide 7
# Compute disparity map
disparity = stereo.compute(left_gray, right_gray)
# Normalize disparity values for better visualization
disparity = cv2.normalize(disparity, None, 0, 255, cv2.NORM_MINMAX)
disparity = disparity.astype(np.uint8)
# Display the disparity map
cv2.imshow('Disparity Map', disparity)
cv2.imshow('left frame', left_frame)
cv2.imshow('right frame', right_frame)
# Exit the loop if the 'q' key is pressed
if cv2.waitKey(1) & 0xFF == ord('q'):
break
# Release both cameras and close the window
left_cap.release()
right_cap.release()
cv2.destroyAllWindows()
Menghitung disparity map
Normalisasi disparitas
Menampilkan disparitas
Menutup loop dengan menekan q